## Slide 1: Microwave Moonbounce Communication. Peter Blair G3LTF

## Slide 2: Contents
Early History of Moonbounce
How does Moonbounce Work?
What are the difficulties and how are they overcome?
EME Systems and components
System Measurement and optimisation

## Slide 3
Notes: 2.6 deg vertical BW

## Slide 4
Notes: 1 deg BW

## Slide 5: All the early efforts were on 144MHz with big co-linears, yagi arrays and stacked Rhombics but with limited success

## Slide 6: The Father of Microwave EME, Sam Harris W1FZJ
Tremendous progress in 1950s in solid state devices, varactor diodes
Parametric Amplifiers then possible up to several GHz
Microwave Associates had paramps, Eimac had klystrons, find some dishes and its ...Game On!

## Slide 7: The Big Bang! QST September '60
W1BU works W6HB on 1296MHz via the moon!
Serious VHF/UHF operators everywhere think.....
“How can I copy that?
What do I need?
How do I build a big enough antenna and how do I point it?
How do I generate the power?”
Etc...etc

## Slide 8: What happened next?
Lots of dishes built and signals copied from W1BU in USA and Europe, but the next full 1296MHz contacts were in 1962 when W1BU worked W2CXY and KH6UK.
First 144MHz QSO April 1964 W6DNG and OH1NL
First 432MHz QSO May 1964 W1BU and KH6UK
June 1964. KP4BPZ using the Arecibo 1000ft dish works 6 stations on 432 MHz including HB9RG and G3LTF.
September 1964. HB9RG works W1BU on 1296MHz
July 1965. KP4BPZ returns on 432MHz, 28 QSOs and ssb

## Slide 9: The 1000ft Spherical reflector at Arecibo used at 432 and 144MHz, KP4BPZ
Notes: 58dBi gain

## Slide 10: 15ft dish at Galleywood Essex, 1963. ( note co-linear stack antennas for 70 & 23cm tropo)

## Slide 11: Now working on 1296MHz, 1968
Notes: 4.8m dish 1968 with circular waveguide feed 19mm mesh Simple wooden hub and arms

## Slide 12: Dish # 2, 1970-1993 0.5 – 0.37 f/D 4.8m>6.5m moved location 3 times
Notes: The arms on this dish, cut from plywood lasted 23 years… next slide

## Slide 13: Today, NW Hampshire, 6m Dish #8, all aluminium, 0.375 f/D 6mm mesh, works at 5760MHz
Notes: 6mm mesh and improved profile in the outer sections meant it worked reasonably well up to 6cm.

## Slide 14: There are only two equations that you need for sucessful EME……
(1) The “radar” equation
S/N = [K*Gr*Gt* Pt] / [R^4* Tsys* Br]
Gr, Gt are the Antenna gains
Pt Transmitter power at the antenna
Tsys System Temperature
Maximising G/T is the key to performance
R moon distance
Br Receiver detection bandwidth
K contains all the boring constants. Equation (2) comes later

## Slide 15: On the path from transmitter to the receiver detector the signal is affected by a number of obstacles
Path Loss
Polarisation change
Geometrical and Faraday Rotation
Ionospheric losses (only at lower frequencies)
Time Delay …… average value 2.5 seconds
Doppler Shift
Signal spreading at microwave frequencies
Noise
Notes: Iono loss at 144 in daylight typically 0.5dB More in disturbed inonosphere or though Auroral zones.

## Slide 16: Path Loss is high but with the same size dish at each end and same power and receive system noise figure….. Higher frequencies give much better signals

## Slide 17: On the path from transmitter to the receiver detector the signal is affected by a number of obstacles
Path Loss
Polarisation change
Geometrical and Faraday Rotation
Ionospheric losses (only at lower frequencies)
Time Delay …… average value 2.5 seconds
Doppler Shift
Signal spreading at microwave frequencies
Noise
Notes: Iono loss at 144 in daylight typically 0.5dB More in disturbed inonosphere or though Auroral zones.

## Slide 18: Geometric Polarisation Rotation

## Slide 19: Faraday Rotation. As a wave travels through the ionosphere its polarisation rotates depending on the total electron density and the magnetic field along its path. The effect varies as wavelength squared. It is negligible above 23cm. Using Circular Polarisation overcomes ALL polarisation problems. CP is used almost exclusively on microwave EME.

## Slide 20: On the path from transmitter to the receiver detector the signal is affected by a number of obstacles
Path Loss
Polarisation change
Geometrical and Faraday Rotation
Ionospheric losses (only at lower frequencies)
Time Delay …… average value 2.5 seconds
Doppler Shift
Signal spreading at microwave frequencies
Noise
Notes: Iono loss at 144 in daylight typically 0.5dB More in disturbed inonosphere or though Auroral zones.

## Slide 21: On the path from transmitter to the receiver detector the signal is affected by a number of obstacles
Path Loss
Polarisation change
Geometrical and Faraday Rotation
Ionospheric losses (only at lower frequencies)
Time Delay …… average value 2.5 seconds
Doppler Shift
Signal spreading at microwave frequencies
Noise
Notes: Iono loss at 144 in daylight typically 0.5dB More in disturbed inonosphere or though Auroral zones. Scales as 1/F^2

## Slide 22: Doppler Shift and Signal Spreading
Doppler shift comes from the relative motion of Earth and Moon, mainly from Earth’s rotation. (Think of the train whistle effect)
Total Doppler shift is the sum of each stations individual Doppler shift
Due to Moon’s slightly eccentric orbit the relative velocity varies at about 0.2m/S. This is called Libration
At microwave frequencies this causes spreading of the signal

## Slide 23
Time, min from Moon rise

## Slide 24: Libration Spreading OK1KIR 6cm
Calculated Libration (by G3WDG) 78Hz

## Slide 25: On the path from transmitter to the receiver detector the signal is affected by a number of obstacles
Path Loss
Polarisation change
Geometrical and Faraday Rotation
Ionospheric losses (only at lower frequencies)
Time Delay …… average value 2.5 seconds
Doppler Shift
Signal spreading at microwave frequencies
Noise
Notes: Iono loss at 144 in daylight typically 0.5dB More in disturbed inonosphere or though Auroral zones.

## Slide 26: Noise
Noise is caused by the random movement of electrons colliding with ions in a conductor
At absolute zero, 0 degrees Kelvin, or minus 273C, no noise is generated.
Noise power ~ kTB k is constant and B is fixed so noise power can be represented by T called the Noise Temperature.
Deepest outer space is close to 0K, actually it’s 3.4K, the remnant of the Big Bang.

## Slide 27: The discovery of the cosmic microwave background in 1964 at Holmdel NJ
By NASA - Great Images in NASA Description, Public Domain
“I still can’t account for that last 3.4K”
Notes: Penzias and Wilson

## Slide 28: Our signal returning from the moon has to battle against NOISE from several sources.
Noise picked up by the antenna together with the signal
Noise generated in any lossy components in the signal path
Noise generated by the amplifier in the receiver system
Other users of the microwave bands, mobile radio / TV and Wi-Fi

## Slide 29: Noise comes into the antenna from the sky via the main beam and from the ground via far-out sidelobes, also called spill-over. A long way down.… but the ground is hot.
Sky background 4-100K depending on frequency and elevation
Ground 300K
Good feed system design minimises this

## Slide 30: The sky temperature,Tsky, is frequency and elevation dependent

## Slide 31: A map at 408MHz of the sky temperature. Today the moon is in a very quiet part of the sky.

## Slide 32: Our signal returning from the moon has to battle against NOISE from several sources.
Noise picked up by the antenna together with the signal
Noise generated in any lossy components in the signal path
Noise generated by the amplifier in the receiver system
Other users of the microwave bands, mobile radio / TV and Wi-Fi

## Slide 33: OZ1LPR 6cm system. Minimal loss from horn to LNA
Relay
LNA
Driver
100W PA
Feed
Transverter

## Slide 34: We must minimise the noise added by the receiver front end. This means a low noise temperature, Trx ( low NF)
G4DDK 23cm VLNA Trx 17K
(0. 24dB)
The clever bit in detail, 13cm.

## Slide 35: G3LTF built 6cm LNA 0.65dB NF (W5LUA design with ATF36077)

## Slide 36: 3cm LNAs
Modified LNB 1dB NF
DB6NT LNA 0.7dB NF

## Slide 37: The big change in 50 years is in the receiver system technology.
My 23cm Parametric Amplifier
7 interacting adjustments!
NF 1-2dB with 20dB gain
Pressurised air-spaced cable, but still about 1dB loss

## Slide 38: Our signal returning from the moon has to battle against NOISE from several sources.
Noise generated in any lossy components in the signal path
Noise generated by the amplifier in the Noise picked up by the antenna together with the signal
receiver system
Other users of the microwave bands, mobile radio / TV and Wi-Fi
Low side-lobes, good RF filtering after the LNA, is about all we can do to combat these sources

## Slide 39: All of the noise contributions add up.
If we think about, and measure, everything in terms of its Noise Temperature then its very easy to work out how good our system is and what is important.
We just add all the temperature contributions, so…..
T system = T sky + T spillover +T loss + T rx
A good system would be about 48K at 23cm and 90K at 3cm.
At 23cm and above T spillover and Trx dominate.
The moon’s thermal noise will contribute as the antenna beamwidth approaches 0.5 degree.

## Slide 40: The second important equation for successful EME…..
10 x 0.1 dB = 1dB
or even more…

## Slide 41: We have some software that does all the calculations of system performance
EMECalc written by the late VK3UM
http://www.vk3um.com/eme%20calculator.html

## Slide 42: EMECalc software estimates EME system performance. VK3UM Software

## Slide 43: EME systems and Components
Antennas and Transmitters
(we covered preamps earlier)

## Slide 44: Antennas for Microwave EME
At 23cm and up reflectors are easily the best
Single feed point allows low losses
Pattern and polarisation can be well controlled
Multiband operation from one antenna
Prime focus, Off-set, Cassegrain
Surface can be solid or mesh
Build-your-own very feasible up to 15m diameter

## Slide 45: Next….Some dishes Large and Small
In the mid 1950s I recall putting some shillings into a tin at the RSGB London VHF club meeting to help pay for this wonderful antenna!

## Slide 46: PA3FXB 3m dish for 23cm
The Dutch are very good at fitting 2.4 -3.5m dishes into their small gardens. Jan also used this for an ISS bounce contact

## Slide 47: The 25m Dish at Dwingelo, Holland restored by the “CAMRAS” team. Used on 70cm to 6cm
Multiband feed system
PI9CAM… CW, SSTV, JTxx , SSB

## Slide 48: Standardised plugs and wing nuts makes feed changing easy for multiband contests. BUT…. a safe access platform is essential
13cm feed, PA below the dish, transverter in the shack
9cm feed, transverter and PA at the feedpoint

## Slide 49: G4CCH 5.4m dish 0.5f/D Operates 70cm to 6cm

## Slide 50: Two compact EME systems, working on 23cm to 3cm and 13cm
G4BAO 1.9m dish
K1DS “Driveway” 3m dish system
G4BAO
23cm 200W
112 initials
34 CW, 2ssb
13cm 210W
49 initials
27CW, 4ssb
9cm 60W
8 initials
2CW
6cm 30W
13 initials
2CW
3cm 12W
3 initials

## Slide 51: Other types of microwave dishes, PA7JB’s offset fed dish and G4NNS’s cassegrain

## Slide 52: 23cm - SSPAs replacing tubes 6x 3CX100A5 800W G4CCH 4x 250W SSPA

## Slide 53: JA4BLC 100W PA for 6cm SM6PGP design

## Slide 54: DL7YC 24GHz system, 2.4m dish
Fully integrated focus box
TWA modified to 24GHz to give 30-50W

## Slide 55: The ultimate in microwave EME 76GHz, Echoes received. See www.microwavers.org RW3BP

## Slide 56: What does a system block diagram look like?

## Slide 57
CP
Feed
Relay
50R Load
LNA
Driver
Transverter
OCXO
144-14MHz
TS850S
Tuneable
Audio
Filter
SDR
PSUs
G3LTF 23cm System
Spectran
400W
96MHz
6x
3CX100A5
PA
Dish Feed-point
Shack
3dB loss
40dB Gain

## Slide 58
CP
Feed
SSPA
Relay
50R Load
LNA
Driver
Transverter
OCXO
144-14MHz
TS850S
Tuneable
Audio
Filter
SDR
Control
PSUs
G3LTF 6cm System
Spectran
4W
40W
87.75MHz
Dish feed-point
Shack

## Slide 59: Operating Modes CW SSB Digital, JTxx

## Slide 60: My preference is CW…. 25kHz of 23cm CW in the ARRL contest

## Slide 61: Many prefer JT65 with a 10-12dB advantage over CW

## Slide 62: System measurement and optimisation
Sun noise measurement gives G/T estimate
Moon noise can give more accuracy
Sun drift through can give beamwidth
Ground to Cold Sky measurement useful but more complex than it first appears
VK3UM’s EMECalc programme can help analyse the results

## Slide 63: NF estimation using cold sky to ground

## Slide 64: Y= [Tsys +Thot] / [Tsys +Tcold] Gives result Tsys = 105-120K Same method used for the antenna but with correction for source (sun / moon) not filling the beam.
Cold Sky Level ~8K
“Hot” absorber, 290K

## Slide 65: Moon noise measurement at 6cm using 6m dish, 1.2-1.3dB

## Slide 66: Thankyou for Listening
Acknowlegements
I am very grateful to Matej, OK1TEH for the use of some of his slides and to many others who have provided pictures and data.

## Slide 67: Some useful EME sites
http://www.df2zc.de/newsletter/ 2m NL
http://www.nitehawk.com/rasmit/em70cm.htm 70cm^NL
http://www.nlsa.com/nets/moon-net-help.html Refl’tor
mailto:moon@moonbounce.info Reflector
http://www.physics.princeton.edu/pulsar/K1JT/ WSST
http://physics.princeton.edu/pulsar/K1JT/Hbk_2010_Ch30_EME.pdf ARRL Handbook EME Section
http://www.moonbouncers.org/ Good tech info
http://www.qsl.net/dk7zb/ Great HB Yagis that work
http://www.hb9q.ch/hb9q/ HB9Q logger
http://www.chris.org/cgi-bin/jt65emeB N0UK logger
http://www.w1ghz.org/antbook/contents.htm Dishes
http://www.vk3um.com/software.html Planner, Analysis++