## Slide 1: RF Power Amplifier Design Considerations for Amateur Radio
Zack Costello | CostelloZD@cardiff.ac.uk | 16th March 2019

## Slide 2: Introduction
Why are RF power amplifiers (PAs) important for amateur radio?
Generate the transmitted power used in transmission – Cannot operate without them!
PA

## Slide 3: Commercial CAD Tools
Most popular industry electronic design automation (EDA) tools:
Keysight Advanced Design System (ADS)
AWR Microwave Office (MWO)
Very powerful tools BUT they are also very expensive, particularly for an individual user

## Slide 4: Free CAD Tools
Looked for software that was free (and ideally open-source):
  What tools are needed for useful PA design software?
  What is currently available?
  What can they do?
  How does it compare against commercial software?

## Slide 5: Talk Aim(s)
Demonstrate some PA design fundamentals using free CAD tools
Will upload files to Cardiff ARS website: https://www.cardiffars.org.uk/
Begin building a learning toolkit similar to those on industry CAD packages to gain greater understanding – But available to all!

## Slide 6: Software Used
Quite Universal Circuit Simulator (Qucs) – Circuit simulator
Several forks…
Can pick and choose tools from each fork
SimSmith – Smith chart tool
GNU Octave – Free alternative to MATLAB
Qucs | Open Source | Linux, MacOS and Windows
Qucs-S | Open Source | Linux and Windows
QucsStudio | Closed Source | Windows only

## Slide 7: FET Transistor

## Slide 8: Current Generator Plane
Cripps, S., 2006. RF Power Amplifiers for Wireless Communications. 2nd Ed. Artech House Inc., p. 30.

## Slide 9: DC-IV Characteristic
Colantonio, P, Giannini, F. and Limiti, E., 2009. High Efficiency RF and Microwave Solid State Power Amplifiers. John Wiley & Sons Inc., p58.

## Slide 10: DC-IV Characteristic
Colantonio, P, Giannini, F. and Limiti, E., 2009. High Efficiency RF and Microwave Solid State Power Amplifiers. John Wiley & Sons Inc., p58.
Apply a DC voltage to the drain-source (VDS): The current will rapidly rise to a value at which it will remain for any further increase in drain voltage – The saturation region

## Slide 11: DC-IV Characteristic
Colantonio, P, Giannini, F. and Limiti, E., 2009. High Efficiency RF and Microwave Solid State Power Amplifiers. John Wiley & Sons Inc., p58.
That saturated value is controlled by the DC voltage applied to the gate (VGS)

## Slide 12: DC-IV Characteristic
Colantonio, P, Giannini, F. and Limiti, E., 2009. High Efficiency RF and Microwave Solid State Power Amplifiers. John Wiley & Sons Inc., p58.
As you reduce the voltage on the gate there will come a point where there is (simply) no more current being drawn – The ‘pinch-off’ (or cut-off) voltage, Vp

## Slide 13: DC-IV Characteristic
DC-IV Characteristic for Qorvo QPD1010 10W GaN Device

## Slide 14: Load Line
To create an output voltage a resistor is needed to complete the circuit: Ropt :
This will allow us to extract the maximum power from a given transistor

## Slide 15: Biasing: ‘Classic’ Amplifier Classes
Colantonio, P, Giannini, F. and Limiti, E., 2009. High Efficiency RF and Microwave Solid State Power Amplifiers. John Wiley & Sons Inc., p42.

## Slide 16: Biasing: ‘Classic’ Amplifier Classes

## Slide 17: Biasing: ‘Classic’ Amplifier Classes

## Slide 18: Generalised PA Architecture – Class AB
Cripps, S., 2012. Amplifier Classes, A to S. In: Walker, J. ed, 2012. Handbook of RF and Microwave Power Amplifiers. 1st ed. Cambridge: Cambridge University Press, Ch. 4, Fig. 4.9.

## Slide 19: Simulation Controllers
The type of simulation controllers is important – They dictate what circuit analysis you can do
For QucsStudio:
  DC – Fundamental
  AC – Linear (small-signal)
  Transient – Solves a set of differential equations that express time dependence of I’s and V’s of circuit
  S-Parameter
  Harmonic Balance
  Parameter Sweeps (used with other controllers)
  Missing Envelope Simulation - Fast and complete analysis of complex signals such as digitally modulated RF signals, has advantages for some applications
QucsStudio can only run one controller at a time

## Slide 20: S-Parameters
Widely used by industry and amateurs alike
Ratio measurements, not absolute measurements
LINEAR

## Slide 21: S-Parameters
(Pink) Reverse measurement, (Blue) Forward measurement
(Left) Extrinsic, (Right) Intrinsic
S. Woodington, Behavioural Model Analysis of Active Harmonic Load-Pull Measurements, Doctoral thesis submitted to Cardiff University. 2012

## Slide 22: Smith Chart Tool
Automated Smith chart tool greatly reduces speed of designing matching networks
SimSmith is a free tool for this purpose
Available at: http://www.w0qe.com/SimSmith.html

## Slide 23: TLine Calculator Comparison
Compared QucsStudios Transmission Line Calculator to ADS LineCalc
Used a Rogers RT/Duroid 5880 to calculate a microstrip line:
  2GHz
  Er = 2.20
  TanD = 0.0009
  Substrate Thickness = 0.508mm
  Conductor Thickness = 35um
https://www.rogerscorp.com/documents/606/acs/RT-duroid-5870-5880-Data-Sheet.pdf

## Slide 24: LineCalc Tool

## Slide 25: QucsStudio – Ideal Transistor
DC-IV simulation of ideal transistor (can specify Vknee and gain)
Idea came from Keysight Technologies YouTube video ‘How to Design an RF Power Amplifier: Class A, AB and B’ (https://www.youtube.com/watch?v=GhPqPVlDRPY) – Worth watching!

## Slide 26: QucsStudio – DC-IV Plot
Vknee = 1V and Imax = 0.5A
Plotted using QucsStudio’s inbuilt data display tool

## Slide 27: QucsStudio – Class B Amplifier
Ideal ‘Class B’ waveforms produced by biasing the transistor appropriately (specify Vgg as shown)

## Slide 28: QucsStudio – Octave Script
Harmonic Balance simulation performed for ideal Class B amplifier shown in previous slide
Problem: Frequency-domain data produced, want to plot the ideal waveforms (convert results to time-domain)
One solution: Octave scripts can be integrated into QucsStudio (and other Qucs branches)! Write script to perform Inverse-Fast Fourier Transforms (IFFTs) on I and V data and plot it
Octave integration gives complete control over data manipulation and display

## Slide 29: QucsStudio – Octave Script
Write script in Octave then set data display in QucsStudio to use the resulting .m file

## Slide 30: QucsStudio – Octave Script

## Slide 31: QucsStudio – Octave Script
These QucsStudio examples are definitely work-in-progress, they simply prove that there is a lot of untapped potential
Should be possible to extend the Octave script to include a GUI (sliders ect) and plot the load-line, giving data display capabilities approaching commercial software equivalents
‘Under-the-hood’ there is more capability available in QucsStudio ect. than shown right now but it is not particularly easy to use (especially for beginners)
A reminder: The files will be available on our website (https://www.cardiffars.org.uk/) – Please contribute to improving this!

## Slide 32: Conclusions
Free tools are available and can be useful
Steeper learning curve, particularly if you have no prior experience
Steadily being improved
You can help right now through creating example workspaces for learning: Share your knowledge!

## Slide 33: Conclusions
Questions?